## Slide 1: Systèmes Embarqués Microprogrammés
NDSerum
Cassien Roth Beneton and Quentin Sandoz

## Slide 2: NDS features: checklist (1/3)
ARM Processors
  ARM9 controls the two screens, buttons except KEY_X / KEY_Y / touchscreen
  ARM7 controls KEY_X / KEY_Y / touchscreen, sound
Timers / Interrupts
  Timer 0 is used by the MaxMod sound streaming mode
  Timer 1 is used by the sound gate functionality
  Timer 2 is used by the wifi connexion status blinking
Graphics
  Main screen: Mode 5 with Backgrounds 0, 2 and 3 (Ext. Rot. and Tiled modes)
  Sub screen: Mode 5 with Backgrounds 0 and 2 (Ext. Rot. and Tiled modes)
Keypad
  Control the wave played and displayed:
    KEY_RIGHT / KEY_LEFT = Change the wave type
    KEY_UP / KEY_DOWN = Change the number of wave periods displayed

## Slide 3: NDS features: checklist (2/3)
    KEY_L / KEY_R = Change the phase of the wave (fine tuning)
    KEY_A = Mute/Unmute the sound
    KEY_X / KEY_B = Increment/Decrement the wave frequency (fine tuning)
    KEY_START = Enable/Disable the wireless sound synchronization
    KEY_Y = Enable/Disable gate effect
  Reading KEY_X / KEY_Y / KEY_START by polling
Touchscreen
  Control of the wave parameters with the sliders/buttons (alternative to the keypad controls)
  Control of the sound gate effect (on/off, gate speed)
  Control of the wifi sync functionality
  Control of the default parameters saving
  Reading touchscreen by polling

## Slide 4: NDS features: checklist (3/3)
Sound
  Playing the wave displayed with the MaxMod sound streaming mode
WiFi
  Possibility to synchronize all the wave properties, the mute functionality and the sound gate between multiple Nintendo DSi
Secondary Storage
  Storing the wave parameters to load at startup in a text file
  Reading the wave parameters to load at startup from a text file

## Slide 5: NDS project screenshot
Include an image with the final view/s of your project on the actual NDS device